## Slide 1
SCARA ROBOT
[Contents]
1. Selection table Robots
- TOSHIBA
- ABB
- YASKAWA
2. External view
- TOSHIBA
- YASKAWA

## Slide 2
1. Selection table Robots

## Slide 3
TOSHIBA
Model |  | THL300
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 300mm(125mm+175mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~160mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 660o/S
 | Axis 2 | 660o/S
 | Axis 3(Z axis) | 1120mm/s
 | Axis 4(Z axis rotation) | 1500o/S
 | Composite | 5.1m/s
Standard cycle time(with 2kg load) |  | 0.48s
Maximum payload mass |  | 5kg(rated : 2kg)
Allowable moment of inertia |  | 0.05kg·m2
Positioning | X-Y | ±0.01mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø4x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 0.7kVA
Mass |  | 12kg

## Slide 4
TOSHIBA
Model |  | THL400
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 400mm(225mm+175mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~160mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 660o/S
 | Axis 2 | 660o/S
 | Axis 3(Z axis) | 1120mm/s
 | Axis 4(Z axis rotation) | 1500o/S
 | Composite | 6.3m/s
Standard cycle time(with 2kg load) |  | 0.47s
Maximum payload mass |  | 5kg(rated : 2kg)
Allowable moment of inertia |  | 0.05kg·m2
Positioning | X-Y | ±0.01mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø4x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 0.7kVA
Mass |  | 13kg

## Slide 5
TOSHIBA
Model |  | THL500
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 500mm(200mm+300mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~150mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 450o/S
 | Axis 2 | 450o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 6.3m/s
Standard cycle time(with 2kg load) |  | 0.45s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.01mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 22kg

## Slide 6
TOSHIBA
Model |  | THL600
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 600mm(300mm+300mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~150mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 450o/S
 | Axis 2 | 450o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 7.1m/s
Standard cycle time(with 2kg load) |  | 0.45s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.01mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 23kg

## Slide 7
TOSHIBA
Model |  | THL700
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 700mm(400mm+300mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~150mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 450o/S
 | Axis 2 | 450o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 7.9m/s
Standard cycle time(with 2kg load) |  | 0.50s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.01mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 24kg

## Slide 8
TOSHIBA
Model |  | THL800
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 800mm(350mm+450mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~150mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 187.5o/S
 | Axis 2 | 217.5o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 4.3m/s
Standard cycle time(with 2kg load) |  | 0.47s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.02mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 33kg

## Slide 9
TOSHIBA
Model |  | THL900
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 900mm(450mm+450mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~300mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 187.5o/S
 | Axis 2 | 217.5o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 4.6m/s
Standard cycle time(with 2kg load) |  | 0.48s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.02mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 35kg

## Slide 10
TOSHIBA
Model |  | THL1000
Type |  | Horizontal milti-joint
No. of controlled axes |  | 4
Arm length |  | 1000mm(550mm+450mm)
Working envelope | Axis 1 | ±125o
 | Axis 2 | ±145o
 | Axis 3(Z axis) | 0~300mm
 | Axis 4(Z axis rotation) | ±360o
Maximum speed | Axis 1 | 187.5o/S
 | Axis 2 | 217.5o/S
 | Axis 3(Z axis) | 2000mm/s
 | Axis 4(Z axis rotation) | 1700o/S
 | Composite | 5.0m/s
Standard cycle time(with 2kg load) |  | 0.48s
Maximum payload mass |  | 10kg(rated : 2kg)
Allowable moment of inertia |  | 0.2kg·m2
Positioning | X-Y | ±0.02mm
repeatability | Z(Axis 3) | ±0.015mm
 | Axisθ(Z-axis rotation) | ±0.007o
Hand wiring |  | 8input / 8outputs
Hand pneumatic joints |  | Ø6x3 pcs.
Position detection |  | Absolute
Robot controller cable |  | 3.5m
Power capacity |  | 1.4kVA
Mass |  | 37kg

## Slide 11
ABB

## Slide 12
YASKAWA
Model |  | MYS450L | MYS650L | MYS850L | MYS1,000L
Type |  | Horizontal milti-joint | Horizontal milti-joint | Horizontal milti-joint | Horizontal milti-joint
No. of controlled axes |  | 4 | 4 | 4 | 4
Arm length |  | 450mm (200mm+250mm) | 650mm (400mm+250mm) | 650mm (450mm+400mm) | 1,000mm (600mm+400mm)
Working envelope | Axis 1 | - | - | - | -
 | Axis 2 | - | - | - | -
 | Axis 3(Z axis) | 0~330mm | 0~330mm | 0~420mm | 0~420mm
 | Axis 4(Z axis rotation) | - | - | - | -
Maximum speed | Axis 1 | - | - | - | -
 | Axis 2 | - | - | - | -
 | Axis 3(Z axis) | - | - | - | -
 | Axis 4(Z axis rotation) | - | - | - | -
 | Composite | - | - | - | -
Standard cycle time |  | - | - | - | -
Maximum payload mass |  | 6kg | 6kg | 10kg | 20kg
Allowable moment of inertia (Normal / Max) |  | 0.01kg·m2 / 0.12kg·m2 | 0.01kg·m2 / 0.12kg·m2 | 0.02kg·m2 / 0.25kg·m2 | 0.02kg·m2 / 0.45kg·m2
Positioning | X-Y | - | - | - | -
repeatability | Z(Axis 3) | - | - | - | -
 | Axisθ(Z-axis rotation) | - | - | - | -
Hand wiring |  | - | - | - | -
Hand pneumatic joints |  | - | - | - | -
Position detection |  | - | - | - | -
Robot controller cable |  | - | - | - | -
Power capacity |  | - | - | - | -
Mass |  | 27kg | 28kg | 46kg | 48kg

## Slide 13
2. External view

## Slide 14
(TOSHIBA-THL300)

## Slide 15
(TOSHIBA-THL400)

## Slide 16
(TOSHIBA-THL500)

## Slide 17
(TOSHIBA-THL600)

## Slide 18
(TOSHIBA-THL700)

## Slide 19
(TOSHIBA-THL800)

## Slide 20
(TOSHIBA-THL900)

## Slide 21
(TOSHIBA-THL1000)

## Slide 22
(YASKAWA-MYS450L)

## Slide 23
(YASKAWA-MYS650L)

## Slide 24
(YASKAWA-MYS850L)

## Slide 25
(YASKAWA-MYS1000L)